## Slide 1: Supersonic Engine Design
Elliott Arpino - AER710 – Propulsion | Fall 2025
A Comparative Study of Turbojet Engines for Supersonic Flight

## Slide 2: Problem Description
Design “fictional” supersonic inlet and engine capable of flying from NY to London in under 3 hours.
Perform a parametric cycle analysis on the “fictional engine”.
Compare the “fictional” supersonic engine, to an “off-the-shelf” supersonic engine.
Mission Requirements | 
Flight Mach (M1) | 3.2
Normal Shock Downstream Mach (M4) | 1.3
# of Shocks at inlet | 4 ( 3 oblique, 1 normal)
Ratio of Specific Heats (γ) | 1.4

## Slide 3: Supersonic Inlet
For the design of the supersonic inlet, an external compression model was selected for the ramp. The shown schematic provides a 2D visual of the model showing key parameters.
Utilizing the flight conditions and requirements, the Oswatitsch principle was used to optimize the inlet.
The Oswatitsch principle states, the pressure recovery in a system (πn) of (n-1) oblique shocks followed by the nth normal shock is maximum when the shocks are of equal strength. When the normal Mach component of each shock is equal.
External Compression Supersonic Inlet

## Slide 4: Supersonic Inlet Design
After iterating the flow turning angle (θ1), then solving a series of compressible flow equations (while forcing the Oswatitsch principle each iteration), a maximum overall pressure recovery was found.
The table shows the key inlet parameters found at the iteration with the highest overall pressure recovery (πd):
Designed Inlet Parameters |  |  |  | 
n | Mn | βn | θn | π n
1 | 3.2 | 27.8° | 11.9° | 0.9320
2 | 2.6 | 35.6° | 14.4° | 0.9320
3 | 2.0 | 50° | 17.2° | 0.9320
4 | 1.3 |  |  | 0.9320
The overall pressure recovery ( π d ) was calculated as 0.79 |  |  |  | 

## Slide 5: “Fictional” Supersonic Inlet Rendition
Modelled using the Designed Inlet Parameters

## Slide 6: “Fictional” Supersonic Engine
Turbojet Engine Schematic
A turbojet was selected as the “Fictional” engine.
Key Turbojet Parameters for Non-Ideal Analysis

## Slide 7: Parametric Cycle Analysis
The parametric cycle analysis of the Fictional Engine was performed with:
    3 different maximum combustion temperatures: 1500 K, 1600 K, 1700 K
    3 different Mach numbers: 0.85, 2, and 3.2
A program was created to iterate across compressor ratios (from 1 - 100), calculating:
    Temperature and Pressure of airflow at each turbojet stage
    TSFC and Specific Thrust
For the “Fictional Engine”

## Slide 8: Parametric Cycle Analysis
Mach 0.85 Results

## Slide 9: Parametric Cycle Analysis
Mach 2.0 Results

## Slide 10: Parametric Cycle Analysis
Mach 3.2 Results

## Slide 11: Compressor Pressure Ratio Selection
For a Flight Mach of 3.2 and Maximum Combustion Temperature of 1600 K

## Slide 12: “Off-the-Shelf” Engine
Pratt & Whitney J58 Engine

## Slide 13: Engine Comparison
“Fictional” vs “Off-the-Shelf”
Not only does the Fictional engine have a greater Specific Thrust, it also has significantly lower TSFC at takeoff.
These improvements come down to more inefficiencies and variables that exist in the real world - that is simply unaccounted for.
Performance Parameter | PWJ58 Engine | Fictional Engine
Type | Turbojet* | Turbojet
Max Combustion Temp. | 1600 K | 1600 K
Compressor Pressure Ratio | 8.8:1 | 5:1
Thrust to mass flow rate at sea-level (kNs/kg) | 0.708 | 0.770**
TSFC at sea-level (kg/Nh) | 0.075 - 0.11 | 0.037**
*PWJ58 is Turbojet but with Ramjet-like qualities at higher Mach numbers. **Numbers were retrieved from parametric cycle analysis at Mach 0 sea-level, since there is no published data on the performance of the PWJ58 at cruise. |  |